EPROM emulator protocol
14 June 2005

CONVENTIONS:
 'X' ==> Ascii char 'X'
 0x12 ==> Hex value
 12 ==> Decimal value

CHECKSUM:
 2's complement of the sum of all the data bytes in the packet.
 Selected so that the sum of the entire packet = 0.

VERSION REQUEST:	ALL H/W AND F/W VERSIONS
_____ _____
| 'V' | CHK |
|_____|_____|

CHK:	Checksum

RESPONSE:
_______ _______ _______ _______
| ERROR | MAJOR | MINOR | HW ID |
|_______|_______|_______|_______|

ERROR:	Error code.
MAJOR:	Major version
MINOR:	Minor version
HW ID:	Hardware ID (0x4D = 512kbit)

GET ID STRING:	ALL H/W AND F/W VERSIONS
_____ _____
| 'G' | CHK |
|_____|_____|

CHK:	Checksum

RESPONSE:
_______ _____ __...__
| ERROR | LEN | IDSTR |
|_______|_____|__...__|

ERROR:	Error code. See list at end of document.
LEN:	Length of ID string
IDSTR:	ID string

BASIC WRITE BLOCK:	ALL H/W AND F/W VERSIONS
_____ _______ _______ _______ _ ... _ _____
| 'W' | ADDRh | ADDRl | COUNT | DATA | CHK |
|_____|_______|_______|_______|_ ... _|_____|

COUNT:	Number of DATA bytes - 1 (up to 255 if RTS/CTS used, max 15 if not)
ADDRh:	Base address high byte
ADDRl:	Base address low byte
DATA:	Data to write
CHK:	Checksum

RESPONSE:
_______ _______
| ERROR | COUNT |
|_______|_______|

ERROR:	Error code.
0x00 = OK (rest of packet sent)
0x01 = Checksum invalid (only result byte sent)
COUNT:	Number of DATA bytes written - 1

SET MODE:	ALL H/W AND F/W VERSIONS
_____ ______ ________ _____
| 'M' | MODE | DEVICE | CHK |
|_____|______|________|_____|

MODE:	Mode identifier
0x00 = LOAD
0x01 = RUN

DEVICE:	Device code
0x00 = 2764	*
0x01 = 27128
0x02 = 27256
0x03 = 27512

CHK:	Checksum

* 2764 = 27128, but data must be loaded twice (as if data had been appended to itself) if a 2764 is being emulated.

RESPONSE:
_______
| ERROR |
|_______|

ERROR:	Error code.

Command 0x00: NOP (ignored, no response). Can be used to re-synchronize the communications link.

ERROR CODES:
0x00 = OK	(complete packet sent)
0x01 = Checksum invalid	(only result byte sent)	[ ANY ]
0x02 = Unsupported command	(only result byte sent)	[ ANY ]
0x03 = Invalid mode identifier	(only result byte sent)	[ 'SET MODE' ONLY ]
0x04 = Invalid device code	(only result byte sent)	[ 'SET MODE' ONLY ]